## Slide 1
Uncooled IR Cameras
Key System Attributes
Fully autonomous system
Dynamic retasking
A/V Weight: <14lbs
Payload: 1-3lbs
Endurance: ~4hrs (payload dependent)
Geo-referenced Imagery
Maximum Altitude 10,000 feet
Operational Altitude 200 ft AGL And Up
Radius of Action 10Km
Cruise Speed 65 Kts
Loiter Speed 32 Kts
Wing Span 48 inches
Video/Data Link C-Band/UHF (mil spec)
Engine Piston, 1-cyl, 1.6 hp
Fuel Type Gasoline
Navigation GPS
Battery 12 / 5 Vdc
Generator 12 volt / 35 watts
BUSTER SUAV is a fully autonomous, high endurance, man-portable system that provides a robust aerial sensor platform for night/day operations. Payloads demonstrated to date include uncooled IR cameras (up to 640 x 480), concurrent side and forward looking imagers (operator selectable), HDTV with full resolution downlink, and an acoustic detection/location system.
BUSTER SUAV
Sensors where you need them, when you need them
Upgrades under investigation:
Heavy Fuel Engine
Communications Relay
On-the-Move C2
HDTV
640x480 UCIR
640 x 480 CCD
320x240 UCIR